## Slide 1: Abnormal detection of Chip Temperature Time Series
GC

## Slide 2: Team members
CAO LIANG
GENG LIANGYU

## Slide 3: Business objective
During burn-in testing, the heat will be generated at the burn-in board, and the temperature of chip on the burn-in board detected by sensor will be increased over the testing time
The abnormal chip temperature during the testing period will have different pattern comparing with normal chip
Normal chips will have a pattern of increasing temperature over time, due to the continuous heating of the oven, and faulty chips will have a different temperate pattern
Faulty chips will be identified by using the abnormal temperature pattern detection

## Slide 4: Burn-In Test
Burn-in Test
  Check the reliability of chips
  Burn-in boards are inserted into the burn-in oven which supplies the necessary voltages to the samples while maintaining the oven temperature

## Slide 5: Burn-In Board
Burn-in Board
  It is used as part of the reliability testing process during which components are stressed to detect failures
  It consist of sockets to accommodate the tested chips and are designed to withstand the hot temperatures during tests

## Slide 6: Technical objective
Create model to perform unsupervised anomaly detection on temperature data
Label chip as normal or faulty based on model output

## Slide 7: Resources
Dataset
  Masked data based on the original data from semi-conductor factory
  Contains sensor temperature data inside IC chip
  Obtained during burn-in test interval under similar testing environment
  Contains 400 burn-in board, and each board contains 32 x 20 chips
  Each chip has 20 temperature reading in 10 minutes interval

## Slide 8: Resources
Dataset

## Slide 9: Resource
Dataset

## Slide 10: Resource
Dataset

## Slide 11: Proposed Approach
Implement unsupervised anomaly detection on temperature time series data
  Temperature time series data will be generated by sensor
  Perform baseline correction on the time series
  Train an auto-encoder on the training temperature data
  Evaluate it on the validation temperature data and the reconstructed error plot
  Choose the threshold and determine the value is abnormal or not
  Label chip as faulty if abnormal value is detected

## Slide 12: Any other additional comment